## Slide 1: Meterrific: Adding Smart Functionality to Traditional Parking Meters
By: Shiv Chopra, Blake Heard, Madison Hester, Michael Knudson, Raj Patel, Andrew Trimper
Date: January 16, 2019
Notes: l

## Slide 2: Introduction
The main goal of Meterrific is to develop a smart add-on for existing parking meters
  Why?
    Address main points or issues with urban street parking
      Minimize time spent and gas wasted looking for parking
      Minimize stress associated with city parking
  How?
    Use sensors to identify spot availability
    Relay information to users
    Navigate to open parking spots near destination
    Re-route users if selected spot becomes unavailable
The team is requesting $164.20 in funding to develop the prototype
Notes: Madison

## Slide 3: Qualitative Goals
Target population: people driving in heavily populated cities with street parking and associated parking meters
Parking Meter
  Protects processing unit from the environment
  Keeps track of overall status and sends status to a cloud database
Mobile App
  Navigates user to the closest parking spot near specified destination
  Receives meter status from cloud database and re-routes user as necessary in real time
  User can pay for the meter through the app
Notes: Shiv

## Slide 4: Design Approach: Hardware
Attachment to existing parking meter
  Interchangeable connection point
  Customizable part between connection point and parking meter
Electronics Housing
  Protects electronics from environmental factors
    Waterproof
    Impact resistance
  Smallest possible size and mass
    Custom 3D-printed component cutouts
    Waterproof Shell
Notes: Andrew

## Slide 5: Design Approach: Electrical
Single printed circuit board (PCB)
  LCD screen, LIDAR, solar panel, sit off-board
  Central microprocessor handles interactions and logic
  Wi-Fi module deals with sending data to cloud
Microprocessor
  Requires: I2C Interface, SPI Interface
  Prototype with Arduino Nano
  Final product uses Atmega328p
Power
  3.7V lithium polymer battery
  Use external voltage regulators
  Use decoupling capacitors
Notes: Andrew

## Slide 6: Quantitative Specs
* Dimensions and cost per unit based on preliminary research. Both are expected to decrease in final product
Resting current draw | ~30mA
Active current draw | ~300mA
Time active (wifi) | < 0.1%
Battery life | 1700 mAh for 300 to 500 cycles
Usage time per battery charge | ~52hrs
Dimensions | 6 in x 3 in x 2 in
Cost per unit | $82.10
Notes: Michael
passive current draws- led, chip
active - wifi

## Slide 7: Design Approach: Software
Parking Meter Add-on Firmware
  Keeping tabs on spot availability
  Power management
  Sending status to database
Cloud Database
  Retrieving and handling of meter status data
Mobile App
  Integration of Pre-existing Maps and Navigation API
  Retrieving and handling of meter status data
Notes: Andrew

## Slide 8: Current Status
Moving to production stage
  Any usability, feasibility, or efficiency discoveries will lead to changes in final design
Finalizing parts requirements and placing orders
Notes: Blake

## Slide 9: Schedule and Next Steps
Notes: Raj

## Slide 10: Questions?